Financial Service Token System
Documentation

# Theory of Operation
## Operation of Module
## Communication protocol

The communication happens over a I2C TWI (Two Wire Interface) and all the packets are broadcast over the network to all the modules present. Each module has an address of 0 and initializes itself as a slave when in an idle state. There are two commands used over the network, one is UPPER_RANGE_CMD, and the other one is CUR_NUM_CMD, each one has 1 argument of 1 byte length. UPPER_RANGE_CMD is sent by the token dispenser to announce that it has just dispensed one more token, the argument carries the number of the token dispensed. This command is received by all counter modules, and the argument is used to update their internal UpperRange variable, to make sure counting stops when that number is reached. All other modules ignore this command. CUR_NUM_CMD is sent by counter modules every time one number is called, and it is received by all other counter modules, which use the argument to update their internal LowerRange variable, to make sure that the receiving module will not count to the same number that has just been called by the sending module. This command is also received by the General Status Monitor which displays the number received in the argument. All other modules ignore this command.
# Hardware
## Parts list
Below is documented the list of parts required to put together one module (not including external pushbutton/power adapter or casing):

Description	Qty.	Element14 part#
Audio Jack	1	35RAPC4BHN2
5V regulator MCP1702	1	MCP1702-5002E/TO
Diode	1	1N4004-T
10uF Capacitor	1	MCMHR16V106M4X7
47uF Capacitor	1	ECA1CM470
10K Resistors	4	SFR16S0001002JA500
RJ45 Jacks	2	MULTICOMP - MTJ-881X1
7-segment decoder HEF4543PTH	2	HEF4543BP,652
Transistor array NPN ULN2003AN	2	ULN2003ANE4
8-pin RMC header	2	N/A came from PDY
2 DIP-SWITCH	1	ADE0204
300 ohm resistor	1	N/A came from PDY
LED	1	N/A came from PDY
100nF Capacitor	1	MCDR50104X7RK0100
20-pin IC base	1	N/A came from PDY
ATtiny2313 Microcontroller	1	ATTINY2313A-PU
LEDs for display	42	N/A came from PDY
68 ohm resistors	14	N/A came from PDY
8-pin RMC cable	2	N/A came from PDY
Main board PCB	1	N/A came from PCB Power
Single digit PCB	2	N/A came from PCB Power

## Schematics & Board layout
## Specifications
## Notes
# Software
## Diagram of version 1
## Notes
## Diagram of version 2
## Notes
# Configuration and Usage
## DIP-switch settings
## Display connections
## Wiring